## Slide 1: Introduction to the prediction of mechanisms
Rich Masel
University of Illinois, Urbana Champaign

## Slide 2: Why Do We Care?
Process chemistry
  What reactions can lead to the desired products
  What side reactions occur
  What are the rates of the processes
  Any safety issues?
Reaction conditions
  Temperature, pressure
  Catalysts, solvents
Contacting pattern
  CSTR vs plug flow
  Mixing issues
  Heat transfer & pressure drop
  Mathematical modeling
In reactor design we need to determine

## Slide 3: We Know How to Calculate
Process chemistry
  What reactions can lead to the desired products
  What side reactions occur
  What are the rates of the processes
  Any safety issues?
Reaction conditions
  Temperature, pressure
  Catalysts, solvents
Contacting pattern
  CSTR vs plug flow
  Mixing issues
  Heat transfer & pressure drop
  Mathematical Modeling

## Slide 4: This Work Gives
Process chemistry
  What reactions can lead to the desired products
  What side reactions occur
  What are the rates of the processes
  Any safety issues?
Reaction conditions
  Temperature, pressure
  Catalysts, solvents
Contacting pattern
  CSTR vs plug flow
  Mixing issues
  Heat transfer & pressure drop
  Mathematical Modeling

## Slide 5: Our Approach to Predict Process Chemistry & Conditions
Develop rules for what reactions can happen
    Ea < 75 kT for initiation reactions
    Ea < 35 kT for propagation reactions
Develop approximations for Ea
Use the findings as a way to quantify process chemistry
Synthesize the results for design

## Slide 6: Rules for mechanisms: Most practical mechanisms must have
Initiation step
    weakest bond in reactants break
Catalytic cycle
    7 generic reaction types
Termination step
Br
H
HBr
Br
2
HBr
H
2
Br
2
All steps have low barriers
    Ea < 75 kT for initiation step
    Ea < 35 kT for propagation step
WeiTi Lee's PhD

## Slide 7: The complete method for mechanism prediction
Figure out what species are possible
  Radicals
  Reactants,Products
Make a list of all possible reactions of those species
Check which reactions must be included
  Initiation reaction
  Catalytic cycle
Eliminate reactions which are slow

## Slide 8: Example H2+ Br2  2HBr
Assume H, Br, H2, Br2, HBr only species
Possible Initiation reactions
H2 + X → 2 H + X
Br2 + X → 2 Br + X
Reactions of H
H2 + H → H + H2
Br2 + H → HBr + Br
HBr + H → H2 + Br

## Slide 9: Example: H2+ Br2  2HBr Continued
Reactions of Br
Br2 + Br → Br + Br2
H2 + Br → HBr + H
HBr + Br → Br2 + H
Termination Reactions
2 Br + X → Br2 + X
H + Br +X → HBr + X
2 H +X → H2 + X
Impossible Reactions
    4 center reactions (Fl, Cl exceptions)
    Reactions without collision partners

## Slide 10: All Possible Reactions
H2 + X → 2 H + X
Br2 + X → 2 Br + X
H2 + H → H + H2
Br2 + H → HBr + Br
HBr + H → H2 + Br
Br2 + Br → Br + Br2
H2 + Br → HBr + H
HBr + Br → Br2 + H
2 Br + X → Br2 + X
H + Br +X → HBr + X
2 H +X → H2 + X

## Slide 11: Rules: Must Have Initiation Reaction
H2 + X → 2 H + X
Br2 + X → 2 Br + X
H2 + H → H + H2
Br2 + H → HBr + Br
HBr + H → H2 + Br
Br2 + Br → Br + Br2
H2 + Br → HBr + H
HBr + Br → Br2 + H
2 Br + X → Br2 + X
H + Br +X → HBr + X
2 H +X → H2 + X
(Need one of these)

## Slide 12: Rules: Must Have Catalytic Cycle
H2 + X → 2 H + X
Br2 + X → 2 Br + X
H2 + H → H + H2
Br2 + H → HBr + Br
HBr + H → H2 + Br (NEED)
Br2 + Br → Br + Br2
H2 + Br → HBr + H
HBr + Br → Br2 + H (NEED)
2 Br + X → Br2 + X
H + Br +X → HBr + X
2 H +X → H2 + X

## Slide 13: Rules: Should Have A Termination Reaction
H2 + X → 2 H + X
Br2 + X → 2 Br + X
H2 + H → H + H2
Br2 + H → HBr + Br
HBr + H → H2 + Br
Br2 + Br → Br + Br2
H2 + Br → HBr + H
HBr + Br → Br2 + H
2 Br + X → Br2 + X
H + Br +X → HBr + X
2 H +X → H2 + X
(Want one of these)

## Slide 14: Rules: Ignore exchange reactions
H2 + X → 2 H + X
Br2 + X → 2 Br + X
H2 + H → H + H2 (Ignore)
Br2 + H → HBr + Br
HBr + H → H2 + Br
Br2 + Br → Br + Br2 (Ignore)
H2 + Br → HBr + H
HBr + Br → Br2 + H
2 Br + X → Br2 + X
H + Br +X → HBr + X
2 H +X → H2 + X

## Slide 15: Rules: Initiation reaction: weakest bond breaks
H2 + X → 2 H + X (104 kcal/mole)
Br2 + X → 2 Br + X (44 kcal/mole)
H2 + X → 2 H + X (Ignore)

## Slide 16: Where are we now?
Br2 + X → 2 Br + X (Need)
Br2 + H → HBr + Br (Need)
H2 + Br → HBr + H (Need)
HBr + Br → Br2 + H
HBr + H → H2 + Br
2 Br + X → Br2 + X (Need)
H + Br +X → HBr + X
2 H +X → H2 + X

## Slide 17: Rules for other reactions
All steps have low barriers
    Ea < 75 kT for initiation step
    Ea < 35 kT for propagation step
    Ea < 40 kT for side reaction
Can calculate minimum temperature for the reaction
Include any other steps which follow the rules

## Slide 18: Polanyi Relationship To Estimate Activation Barriers
"If someone claims to have a general correlation for
reaction rates the prudent engineer should be suspicious"
L.D. Schmidt, 1998
Polanyi relationship
r
p
o
a
a
H
E
E


+
=
2 parameter equation

## Slide 19: Blowers-Masel Equation
1 parameter equation




2
r
2
o
2
p
2
r
o
P
r
o
a
H
w
4
V
H
w
2
V
H
w
2
E









Parameter related to intrinsic barrier
Bond Dissociation Energy
Heat of reaction

## Slide 20: Gives Reasonable Results

## Slide 21: Table of Parameters
Table 5.4 Intrinsic barriers and transfer.
Coefficients for different types of reaction of neutral species.
Reaction
Example
Actual
kcal/mole
to
assume when predicting mechanisms kcal/mole
Actual P
P to assume when predicting mechanisms
Simple bond scission
AB+XA+B+X
X=a collision partner
0-1
1
1.0
1.0
Recombination
A+B+XAB+X
X=a collision partner
0-1
1
0.0
1.0
Exothermic atom
transfer reaction
R x + R1  R + x-R1
x = an atom
8-16
12
0.2 to 0.6
0.3
Endothermic atom
transfer reaction
R- x + RR + x-R1
x=an atom
8-16
12
0.4 to 0.8
0.7
Ligand transfer
reaction to hydrogen
H+R-R1  HR + R1
40-50
45
0.4 to 0.6
0.5
Other ligand transfer reactions
x + R-R1  xR+ R1
x=an atom
50 or more
50
0.3 to 0.7
0.5

## Slide 22: Where are we now?
Br2 + X → 2 Br + X (Need)
Br2 + H → HBr + Br (Need)
H2 + Br → HBr + H (Need)
HBr + Br → Br2 + H (Ea=7 kcal/mole)
HBr + H → H2 + Br (Ea=43 kcal/mole)
2 Br + X → Br2 + X (Need)
H + Br +X → HBr + X
2 H +X → H2 + X

## Slide 23: Rules for other reactions
All steps have low barriers
    Ea < 75 kT for initiation step
    Ea < 35 kT for propagation step
    Ea < 40 kT for side reaction
Can calculate minimum temperature for the reaction
Include any other steps which follow the rules

## Slide 24: More Complex Cases: Additional Reactions
Other classes of reactions
Ligand Transfer Reactions
Beta-scissions
Association Reactions
Addition Reactions
Disproportionations
Isomerization Reactions (5-center)
All the same rules apply

## Slide 25: More Complex Examples: Need To Reduce Number Of Species Considered
Simplified Method
Find a feasible initiation step
Find all feasible reactions of radicals produced in initiation step
Continue generating reactions until I get to desired products
Make sure reaction follows rules
Automated mechanism generation

## Slide 26: Example: CH3CH3  H2C=CH2 + H2
Steps
Find a feasible initiation step
Find all feasible reactions of radicals produced in initiation step
Continue generating reactions until I get to desired products
Make sure reaction follows rules
Automated mechanism generation

## Slide 27: Initiation step: weakest bond breaks in the reactants
C
C
H
H
H
H
H
H
89 kcal/mol
102 kcal/mol

X
CH
2
X
CH
CH
3
1
3
3
+
·
·
+
Initiation step is

## Slide 28: Possible mechanism for CH3CH3  H2C=CH2 + H2

X
CH
2
X
CH
CH
3
1
3
3




3
2
4
2
3
3
3
CH
CH
CH
CH
CH
CH





X
H
CH
CH
X
CH
CH
2
2
3
3
2






3
2
2
4
3
3
CH
CH
H
CH
CH
H





3
3
5
3
CH
CH
X
CH
2


=

## Slide 29: Does the Mechanism Fit All of the Rules?
Diagram the mechanism, estimate the activation barrier for each step and ask whether the mechanism follows the rules
Procedure:

X
CH
2
X
CH
CH
3
1
3
3




3
2
4
2
3
3
3
CH
CH
CH
CH
CH
CH





X
H
CH
CH
X
CH
CH
2
2
3
3
2






3
2
2
4
3
3
CH
CH
H
CH
CH
H





3
3
5
3
CH
CH
X
CH
2


=

## Slide 30: Solution I: Diagram Mechanism

## Slide 31: Solution II: Estimate activation barriers
3
2
4
3
3
3
CH
CH
CH
CH
CH
CH





First Estimate heat of reaction
)
CH
CH
(
H
3
2
f

Therefore
H
r

Next Use Blowers -Masel to Estimate Activation Barrier
E = 8.7 kcal/mol
A
= -17.9 +28.4 -34.8 -(-20.0) = -4.3 kcal/mole
=28.4 kcal/mole


Hf (CH3 ) = +34.8kcal/mole

Hf (CH4 ) = -17.9 kcal/mole

Hf (CH3 CH3 ) = -20.0 kcal/mole


Hf ( CH2 CH3 ) = +28.4 kcal/mole
Data from NIST Webbook

## Slide 32: Is that a low enough activation energy?
All steps must satisfy
    Ea < 75 kT for initiation step
    Ea < 35 kT for propagation step
Energy low enough if temperature high enough
Can Calculate feasible process temperatures!

## Slide 33: Does Another Reaction Occur?





3
4
6
3
3
CH
CH
CH
CH
H
Step does not satisfy criterion: rate negligible
=37.48 Kcal/mole
E
A

## Slide 34: What Are Side Reactions?
Seven generic reaction types
All steps must satisfy
    Ea < 70 kT for initiation step
    Ea < 35 kT for propagation step
Find other steps that satisfy constraints

## Slide 35: Bridge to catalysis
Rules also work on metal surfaces
Blowers-Masel works On Metals
  Assume a possible catalyst (try all metals)
  Heat of reaction changes because catalyst binds intermediates
  Calculate temperature where all criterion satisfied
  Lowest temp is best catalyst - need to also check side reactions
Does not work on acid catalysts
  need new rate laws

## Slide 36: Summary
Can predict mechanisms
Can predict process temperatures
Can use results to predict catalysts