## Slide 1: Ultrasound Imaging
Atam Dhawan

## Slide 2: Ultrasound
Sound waves above 20 KHz are usually called as ultrasound waves.
Sound waves propagate mechanical energy causing periodic vibration of particles in a continuous, elastic medium.
Sound waves cannot propagate in a vacuum since there are no particles of matter in the vacuum.
Sound is propagated through a mechanical movement of a particle through compression and rarefaction that is propagated through the neighbor particles depending on the density and elasticity of the material in the medium.
The velocity of the sound in
  Air: 331 m/sec; Water: 1430 m/sec
  Soft tissue: 1540 m/sec; Fat: 1450 m/sec
Ultrasound medical imaging: 2MHz to 10 MHz
  2 MHz to 5 MHz frequencies are more common.
  5 MHz ultrasound beam has a wavelength of 0.308 mm in soft tissue with a velocity of 1540 m/sec.

## Slide 3: Sound Propagation
Tissue | Average Attenuation Coefficient in dB/cm at 1 MHz | Propagation Velocity of Sound in m/sec
Fat | 0.6 | 1450
Liver | 0.8 | 1549
Kidney | 0.95 | 1561
Brain | 0.85 | 1541
Blood | 0.18 | 1570
The attenuation coefficients and propagation speeds of sound waves.

## Slide 4: Sound Velocity
The velocity of a sound wave in a medium, c, is related to its wavelength  and frequency  by
  c=

## Slide 5: The Wave Equation
If a small force F is applied to produce a displacement of u+u in the x-position on the right-hand side of the small volume. A gradient of force
is thus generated across the element.
where  is the density of the medium and
is the compressibility of the medium.

## Slide 6: Acoustic Impedance
where k is the wavenumber and equal to with wavelength .
The pressure wave that results from the displacement generated is given by
The particle speed and the resulting pressure wave are related as
where Z is the acoustic impedance defined as the ratio of the acoustic pressure wave at a point in the medium to the speed of the particle at the same point. Acoustic impedance Z is the characteristic of the medium as

## Slide 7: Acoustic Transmission

## Slide 8: Multilayered Propagation
A path of a reflected sound wave in a multilayered structure.
x1
x2
x3
I0
R0
T1,2
T3,4
T2,3
T4,3
T3,2
T5,4
Z1
Z2
Z3
Z4
Z5
T2,1

## Slide 9: Reflection and Transmission
Refection and Transmission with acoustic impedances
Since 1+Rij = Tij,,

## Slide 10: Transducer and Arrays
Array of
elements
Beam wavefront
Beam direction
Group 1
Group 2
Group 3
Group 1
Group 2
Group 3


x
x
x
x
x
x

Group 1
Group 2
Group 3

x
x
x

…
…
…
…
…
…

## Slide 11: Imaging System
A schematic diagram of a conventional ultrasound imaging system
Piezoelectric crystal
Acoustic absorbers
Blockers
Imaging
Object
Transmitter/
Receiver
Circuit
Control
Circuit
Pulse
Generation and Timing
Data-Acquisition
Analog to Digital Converter
Computer
Imaging Storage and Processing
Display

## Slide 12: Data Collection
Let us assume that a transducer provides an acoustic signal of s(x,y) intensity with a pulse that is transmitted in a medium with an attenuation coefficient,  and reflected by a biological tissue of reflectivity R(x,y,z) with a distance z from the transducer. The recorded reflected intensity of a time varying acoustic signal, Jr(t) over the region R can then be expressed as:
and c, respectively, represent received pulse and the velocity of the acoustic signal in the medium.

## Slide 13: Data Collection ..
The compensated recorded reflected signal from the tissue, Jcr(t) can be simplified to

## Slide 14: Ultrasound Imaging
An ultrasound transducer provides brief pulses of ultrasound when stimulated by a train of voltage spikes of 1-2 msec duration applied to the electrodes of the piezoelectric crystal element.
An ultrasound pulse
  A few cycles long: 2-3 cycles.
As the same crystal element is used as the receiver, the time between two pulses is used for detecting the reflected signal or echo from the tissue.

## Slide 15: A-Mode Scan
A-Mode scan:
  Records the amplitude of returning echoes from the tissue boundaries with respect to time. In this mode of imaging the ultrasound pulses are sent in the imaging medium with a perpendicular incident angle.
  Since the echo time represents the acoustic impedance of the medium and depth of the reflecting boundary of the tissue, distance measurements for the tissue structure and interfaces along the ultrasound beam can be computed.
  The intensity and time measurements of echoes can provide useful three-dimensional tissue characterization.

## Slide 16: M-Mode Scan
M-Mode Scan
  Provides information about the variations in signal amplitude due to object motion.
  A fixed position of the transducer, in a sweep cycle, provides a line of data that is acquired through A-mode.
  The data is displayed as a series of dots or pixels with brightness level representing the intensity of the echoes.
  In a series of sweep cycles, each sequential A-line data is positioned horizontally.
  As the object moves, the changes in the brightness levels representing the deflection of corresponding pixels in the subsequent sequential lines indicate the movement of the tissue boundaries.
  The x-axis represents the time while the y-axis indicates the distance of the echo from the transducer.

## Slide 17: M-Mode Image
M-Mode display of mitral valve leaflet of a beating heart

## Slide 18: B-Mode Scan
B-Mode Scan
  Provides two-dimensional images representing the changes in acoustic impedance of the tissue.
  The brightness of the B-Mode image shows the strength of the echo from the tissue structure.
  To obtain a 2-D image of the tissue structure, the transducer is pivoted at a point about an axis and is used to obtain a V-shape imaging region. Alternately, the transducer can be moved to scan the imaging region.
  Several images of the acquired data based on the processing kernel filters can be displayed to show the acoustic characteristics of the tissue structure and its medium.

## Slide 19: B-Mode Image
The “B-Mode” image of a beating heart with mitral stenosis.

## Slide 20: Mitral Valve

## Slide 21: Doppler Image
A Doppler image of the mitral valve area of a beating heart.
where v is the velocity of the moving source or object, f is the original frequency, c is the velocity of the sound in the medium, and is the incident angle of the moving object with respect to the propagation of the sound.