## Slide 1: RELIABILITY: CHAPTER 13
RELIABILITY ENGINEERING

## Slide 2: PRODUCT PERFORMANCE
Product performance is influenced by the following two sets of factors:
(i) Factors prior to the sale of the product
(ii) Factors during product use
The manufacturer has reasonable control over (i) and no (or limited) control over (ii).

## Slide 3: PRODUCT PERFORMANCE
For most products the characterization of product performance requires a multi-dimensional vector. Several components of this vector are related to product reliability. These include various notions of reliability, dependability, availability and so on.

## Slide 4: RELIABILITY ENGINEERING
Reliability engineering deals with the design and manufacture (or construction) of products (systems) taking into account the unreliability of its parts and components.
It also includes reliability testing and programs to improve reliability.

## Slide 5: RELIABILITY ENGINEERING
These efforts must be done in a manner so that they fit into the overall business context and take into account the technological and commercial aspects and their interaction. Good engineering of a product requires that this be done during the design stage to ensure that the product produced is reliable.

## Slide 6: ENGINEERING
Engineering can be defined as the professional art of applying science to produce new products which meet the stated requirements in terms of technical performance and commercial constraints -- for example, building a new computer chip with a specified speed and for release by a specified target date.

## Slide 7: ENGINEERING PROCESS
The engineering process to achieve this involves the following three phases:
(i) Design and development
(ii) Manufacturing (Construction)
(iii) Pre-sale (pre-delivery) assurance
These are sequentially linked and there are several stages in each phase.

## Slide 9: DESIGN AND DEVELOPMENT PHASE
Deals with the processes which leads to a prototype version of the product that meets the stated technical requirements and can be manufactured (constructed) in a manner that satisfies the stated commercial constraints.
This phase determines the quality of “product performance”.

## Slide 10: MANUFACTURING [CONSTRUCTION] PHASE
The manufacturing phase deals with the process necessary to produce items in bulk in such a manner that all items conform to the stated design performance and to achieve this in the most economical manner.
The focus in this stage is on the control of reliability degradation.

## Slide 11: PRE-SALE (-DELIVERY) PHASE
The main aim of this phase is on testing to assure product performance. For complex expensive products involving new technologies and custom built (e.g., specialized defense products), this phase is very important and explicitly addressed in the contract between the manufacturer and the buyer.

## Slide 12: DESIGN AND DEVELOPMENT PROCESS

## Slide 13: DESIGN AND DEVELOPMENT PROCESS
The design and development process can be viewed as the consolidation of resources (e.g., human, material, technologies) and information (e.g., customer needs, business goals) into a product that meets the customer needs and achieves the business goals.

## Slide 14: DESIGN PROCESS
BUSINESS
STRATEGY
DESIGN
PROCESS
MANUFACTURING
PHASE
RELIABILITY
THEORY
TECHNOLOGY
POST-SALE
SERVICE
CUSTOMER
NEEDS
COST
ANALYSIS
MANUFACTURABILITY

## Slide 15: DESIGN AND DEVELOPMENT PROCESS
The design and development involves the following four stages:
- Requirement definition
- Conceptual design
- Detailed design
- Testing and evaluation

## Slide 16: REQUIREMENTS DEFINITION
The requirement definition identifies the overall needs of the user and defines the objectives for the product.
For defense products -- the requirement definition is provided by the buyer.
For consumer durables and industrial products, the manufacturer decides on these based on a market survey.

## Slide 17: CUSTOMER SATISFACTION
“Customer satisfaction is essential to survival in today’s global dynamic competition. The ultimate proof of a product design is the acceptance by the customer. Only those companies that listen to what the customer wants and provide high-quality and reliable products, which meet customer expectations, over the product useful life period with minimum cost in a timely fashion, will eventually survive.” [Wang]

## Slide 18: SATISFACTION PARAMETERS
They include:
Product performance specifications (e.g., efficiency, output level etc.)
Product conformance to specifications
Product reliability (mean time to failure, mean time to repair, durability, longevity, etc.)

## Slide 19: SATISFACTION PARAMETERS
Technical assistance (e.g., manuals, training programs)
Price and value for money
Post-sale service (warranties, spares, repair service)
Complaint resolution (for problems encountered)

## Slide 20: CONCEPTUAL DESIGN
During this stage, different design approaches and technologies are evaluated with regards their capabilities to ensure that a product which embodies these is capable of meeting all the requirements of (i) perform- ance as stated in the requirement definition, (ii) manufacturability and, (iii) unit manufacturing cost.

## Slide 21: CONCEPTUAL DESIGN
The goal of this stage is to decide on the optimum design approach in fairly general terms. This is done by carrying out the following activities:
- Trade-off studies,
- Mathematical and simulation models
- Cost analysis

## Slide 22: TRADE-OFF STUDIES
Design trade-off studies examine alternative designs to optimize the overall performance and at the same time reduce the technical risk. The latter is very important when the design involves new and untested technologies.

## Slide 23: COST ANALYSIS
There are many different types of cost analysis.
Two commonly used analysis are:
(i) Design to cost (DTC)
(ii) Life cycle cost (LCC).

## Slide 24: DESIGN TO COST
In the design to cost methodology, the aim is to minimize the unit manufacturing cost. This cost includes the cost of design and development, testing and manufacturing.
This is used to achieve the business strategy of a higher market share through increased sales for consumer durables and many industrial and commercial products.

## Slide 25: LIFE CYCLE COSTS
In the life cycle cost methodology, the cost includes the total cost of acquisition, operation and maintenance over the life of the item and the cost associated with its discarding at the end of its useful life.
This is used for expensive defense and industrial products.

## Slide 26: OUTPUTS OF CONCEPTUAL DESIGN STAGE
Guidelines,
Design requirements,
Program plans, and
Other documentation
that will provide a baseline for the activities at the next stage (detailed design) of the design process

## Slide 27: DETAILED DESIGN AND DEVELOPMENT
The detailed design begins with an initial design that is subjected to a detailed analysis. Based on the analysis, the design is improved and the process is repeated until the analysis indicates that the performance requirements are met.
This analysis involves many elements:

## Slide 28
ENVIRONMENTAL ANALYSIS
MECHANICAL STRESS ANALYSIS
THERMAL ANALYSIS
DESIGN REQUIREMENTS AND ANALYSIS
RELIABILITY ALLOCATIONS
TESTABILITY ANALYSIS
PRODUCIBILITY ANALYSIS
FACILITY REQUIREMENTS
SUPPORTABILITY AND MAINTAINABILITY ANALYSIS
DESIGN
TRADE OFFS
LIFE
CYCLE
COST
DESIGN
TO
COST
RELIABILITY
PREDICTION
DESIGN POLICY/ CRITERIA
FAILURE MODE EFFECTS AND CRITICALITY ANALYSIS
WORST CASE ANALYSIS
PACKAGING ANALYSIS
SNEAK CIRCUIT ANALYSIS
BIT + ATE ANALYSIS
BREADBORDING RESULTS
HUMAN FACTORS
SAFETY

## Slide 29: DETAILED DESIGN AND DEVELOPMENT
The final design must achieve a proper balance between performance, technical risk, cost, manufacturability and other parameters.
This requires detailed modeling and analysis by specialists from different engineering disciplines.

## Slide 30: DETAILED DESIGN AND DEVELOPMENT
It is important to discover all potential problems with the product and fix these during this stage of the design process. If not, the cost of changes to the design increases significantly.
A design change during the manufacturing phase is roughly 2 - 10 times more costly.
A design change after the product is released to the buyers is roughly 10 - 100 times more costly.

## Slide 31: OUTPUTS OF DETAILED DESIGN STAGE
The outputs of the detailed design stage are design documents for use in the manufacturing (construction) phase.
These deal with issues such as
- Product characterization in terms of sub-systems, modules, etc., down to the part level.

## Slide 32: OUTPUTS OF DETAILED DESIGN STAGE
- Performance specification at different levels
- Material selection at the part level
- Assembly of parts into modules, sub-systems, etc., leading to the final system
- Testing at different levels to evaluate performance

## Slide 33: KEY DESIGN PRACTICES
At the requirement definition stage, key design practices establish the following points:
1. User needs are evaluated and documented.
2. Realistic operational requirements are developed into product use profiles. These deal with the environments in which products must perform.

## Slide 34: KEY DESIGN PRACTICES
At the conceptual design stage, key design practices provide the following:
1. Design requirements based on user needs, operational requirements, and product use profiles.
2. Design goals are stated in easily understood, design oriented terms.
3. Design requirements are frozen at the end of conceptual design.

## Slide 35: KEY DESIGN PRACTICES
At the detailed design stage, key design practices provide the following:
1. Design analyses and trade-off studies which take into account manufacturability and post-sale issues.
2. Stress analysis to evaluate product performance under different environments.

## Slide 36: DESIGN REQUIREMENTS FOR RELIABILITY
In order to ensure that the design process produces a product which meets these reliability related performance measures, one needs to define reliability goals at the requirements definition stage. During the conceptual and detailed design stages, one needs to address various reliability related decision issues.

## Slide 37: RELIABILITY GOALS
The reliability goals must compete with other performance and commercial goals during the formulation of a new product strategy. As such, for the reliability goals to receive proper management attention, they must be realistic, understandable, measurable and verifiable throughout the design and development stage.

## Slide 38: SETTING RELIABILITY GOALS
Several different bases:
Arbitrary Goals: These can be either qualitative or quantitative, as for example
(i) Failure rate less than 0.1 per year over the warranty period,
(ii) Expected warranty cost less than 0.5% of the sale price,
(iii) Mean time to repair less than 3 hours

## Slide 39: SETTING RELIABILITY GOALS
Market Sensitivity Assessment Based Goals: This is based on a (usually fairly vague) in-house opinion with regard to market sensitivity to certain reliability related issues. As an example, every second item failing within the first six months might be deemed as being a “major disaster” where as one in a hundred items sold causing minor trouble would be “ideal”.

## Slide 40: SETTING RELIABILITY GOALS
End Product and Company Requirements: These deal with the long term reliability goals and warranty performance of the end product. This involves warranty trend analysis. The reliability goal is linked to the end product requirements. For example, the current warranty cost may be 5% of the sale price, with the reliability goal in the long term being to reduce this to 3% in two years and to less than 1% in five years.

## Slide 41: SETTING RELIABILITY GOALS
Reliability Goals Based on Past Performance: This is appropriate when, due to new technology, an existing product is replaced by a new product which does essentially the same function as the old one. The reliability goals are set to achieve a higher reliability based on the benefits of the new technology. As an example, reducing the expected number of failures in the first twelve months from 0.05 to 0.03.

## Slide 42: SETTING RELIABILITY GOALS
Reliability Cost Optimization Based Goals: The total cost is the sum of the following three costs -- (1) cost of reliability design (a function of the number of cycles needed for achieving the reliability), (2) cost of reliability production (fixed and variable cost to control reliability during manufacturing), and (3) warranty cost (which depends on the environment and usage intensity). The reliability goal is selected to minimize this total cost.

## Slide 43: RELIABILITY ISSUES [CONCEPTUAL DESIGN STAGE]
The process of dividing the system reliability goal into sub-system and component reliability goals is called reliability allocation or reliability apportion- ment.
The reliability allocation to various sub-systems must be compatible with their current state of development, expected improvement, and the amount of testing effort (in terms of time and money) needed for the development.

## Slide 44: RELIABILITY ISSUES [CONCEPTUAL DESIGN STAGE]
It must be done in a manner so as to achieve the desired system reliability at minimum cost or maximum system reliability for a given development budget.
Often, achieving the desired reliability at component or sub-system level requires development to improve the reliability. This is also known as reliability growth.

## Slide 45: RELIABILITY ISSUES [DETAILED DESIGN STAGE]
At the detailed design stage, reliability prediction is the important issue. This is a process used for estimating the reliability of a design prior to manufacturing and testing of produced items. Reliability predictions provide a basis for evaluating reliability growth during the development stage.
One can assess the actual reliability achieved, by testing. This process is called reliability assessment.

## Slide 46: OTHER RELIABILITY ISSUES
Product reliability is degraded during manufacturing and is influenced by the operating environment and operational mode.
Engineers must consider operational and environmental envelopes (rather than a single value) in determining the reliability requirements.

## Slide 47: OTHER RELIABILITY ISSUES
Reliability Design Review
This is a review of the reliability of the final design so as to ensure that the reliability goals have been achieved. This must performed independently. Lloyd and Lipow (1962) give a checklist for effective reliability design review. Issues that must be dealt with are:

## Slide 48: Reliability Design Review
What are the critical weaknesses? What provision has been made in the design so that modifications can be made at the earliest possible time if these and other weaknesses show up in testing?
Has the product been designed as simply as possible? Have human factors been considered to prevent errors such as reversed wiring for an electronic product or misassembly for a mechanical product?

## Slide 49: DESIGN FOR QUALIFICATION [ELECTRONIC EQUIPMENT]
This involves the following steps:
1. Define realistic system requirements.
2. Define the system usage environment.
3. Identify the potential failure sites and failure mechanisms.
4. Characterize the materials and the manufacturing and assembly processes.

## Slide 50: DESIGN FOR QUALIFICATION [ELECTRONIC EQUIPMENT]
5. Design reliable products within the capabilities of the materials and manufacturing processes used.
6. Qualify the manufacturing and assembly processes.
7. Control the manufacturing and assembly processes.
8. Manage the life cycle usage of the product.

## Slide 51: MANUFACTURE [CONSTRUCTION]

## Slide 52: RELIABILITY DEGRADATION
The reliability of manufactured products produced will, in general, differ from that predicted by the design and of the prototype produced under strict laboratory conditions.
Items which conform to the design specifications are called “conforming” and others are “non-conforming”.

## Slide 53: RELIABILITY DEGRADATION
The causes for the degradation can be categorized into two groups:
1. Variations due to uncontrollable causes. By and large nothing can be done about this source of variation, except to modify the process.
2. Variations due to assignable causes in the production process, input material and/or human operators.

## Slide 54: NON-CONFORMANCE - I
The failure distribution of conforming items is given by F(t), with the failure rate constant up to a point tf and increasing beyond tf.
The failure distribution of non-conforming items is given by F1(t) which differs from F(t) as follows. The failure rate is decreasing up to ti < tf and is same as that for conforming items beyond ti.

## Slide 55: FAILURE RATE
r(t)
tf
time

## Slide 56: FAILURE RATES
r(t)
time
NON-CONFORMING
CONFORMING

## Slide 57: FAILURE RATE
r(t)
ti
tf
time

## Slide 58: NON-CONFORMANCE - I
An explanation for this is as follows. In general, most products are composed of several parts. Even with all the parts conforming to design specifications, an item can fail early due to chance errors in the assembly process (e.g., misalignment, dry solder joint, and so on). This increases the failure rate during the initial life of items. These types of failures are also termed “teething problems”.

## Slide 59: NON-CONFORMANCE -II
Conforming items have a failure rate which conforms to the design specification.
Non-conforming items have a failure rate which is greater than that for conforming items.
Let p denote the probability that an item is conforming.

## Slide 60: NON-CONFORMANCE -II
Let F(t) [F2(t)] denote the failure distribution of conforming [non-conforming] items.
The failure distribution of items produced is given by

## Slide 61: RELIABILITY CONTROL
Reliability control deals with mechanisms to control the degradation of reliability during manufacturing.
Two approaches for control:
- Weeding: To weed out non-conforming items
- Prevention: To minimize the occurrence of non-conforming items

## Slide 62: TESTING

## Slide 63: TESTING
Testing can be defined as the application of some form of stimulation to a system (or sub-system, module or part) so that the resulting performance can be measured and compared with the design requirements.

## Slide 64: TESTING
One can group testing into three categories:
1. Developmental Testing
2. Manufacturing Testing
3. Field and Operational Testing

## Slide 65: DEVELOPMENTAL TESTING
Some of the tests carried out during product development are as follows:
1. Testing to Failure
2. Environmental and Design Limit Testing
3. Accelerated Life Testing
4. Critical Evaluation and Part Qualification Testing

## Slide 66: MANUCTURING TESTING
Some of the tests carried out during manufacturing are as follows:
1. Environmental Stress Screening
[ESS]
2. Burn-In

## Slide 67: Field and Operational Testing
Such tests provide useful data relating to product reliability and performance in the real world.
Operational field testing is a joint effort involving the manufacturer and buyers.

## Slide 68: TESTABILITY
Testability is a concept closely related to testing. It is a process through which a failure in a system can be detected and identified so that corrective actions can be initiated to rectify the failure. If the failure is due to an external factor then testability allows for its detection and identification.

## Slide 69: TESTABILITY
Testability can be either built into the product (called BIT -- built-in=test) or it can be carried out by equipment external to the product.
For complex electronic systems, testability can be done at different levels ranging from the system level down to the part level.

## Slide 70: BURN-IN
Burn-in is a mechanism to improve product reliability by consuming a part of the useful lifetime of each item. The process of burn-in involves testing items for a period  (called the burn-in period).
Burn-in is used to improve the reliability of the product.

## Slide 71: BURN-IN
Let F(t) [G(t)] denote the failure distribution before [after] burn-in and  the burn-in time. Then,
For burn-in to be effective, G(t) must be superior to F(t).