## Slide 1: RELIABILITY: CHAPTER 11
MODEL SELECTION
AND VALIDATION

## Slide 2: MODEL SELECTION & VALIDATION
This means choosing a “best” model from a set of candidate models and then validating this choice, i.e., providing evidence that the chosen model is, in fact, adequate and valid for the intended reliability objective.
Notion of “valid” and “invalid” models.

## Slide 3: MODEL SELECTION & VALIDATION
The procedures can be graphical and/or analytical.
The latter involves statistical hypothesis testing.
An invalid model yields results which are meaningless in the context of the reliability study.

## Slide 4: GRAPHICAL METHODS
Graphical methods of model selection involve preparation of probability plots or other graphs, such as hazard plots, and checking visually to determine whether or not the plots appear to show certain characteristics indicative of a particular model.

## Slide 5: GOODNESS-OF-FIT TEST
These are statistical procedures for testing hypothesized distributions and/or models. Note, incidentally, that a poor fit (either graphical or analytical) may occur for two reasons: (1) the model is incorrect, or (2) the model is correct, but the parameter values specified or estimated may differ from the true values by too great an amount.

## Slide 6: MODEL SELECTION & VALIDATION
Note that in both the selection and validation processes, particularly when graphical methods are employed, both art and science are involved. The art part is especially apparent in visual fitting of data to a model.

## Slide 7: MODEL SELECTION & VALIDATION
Subjective decisions must be made in the analysis.
This includes selection of models to be considered, selection of a level of significance in statistical testing, which statistical procedures are to be used, and so forth.

## Slide 8: GRAPHICAL METHODS
In the graphical method, the main objective is to “fit” data to one or more of the probability distributions (or, conversely, to “fit” the distributions to data).
Visual fits provided by graphical methods are quite useful for this purpose,

## Slide 9: GRAPHICAL METHODS
There are many plotting papers, computer algorithms and other aids in plotting data under specific distributional assumptions.
Many of these also provide graphical techniques for estimating the parameters of the assumed distribution.

## Slide 10: GRAPHICAL METHODS
Benefits of this approach are the visual insights obtained and (usually) ease of application, particularly in the case of a number of distributions, including the exponential, Weibull, normal, extreme value, and others, for which plotting and computer aids are available.

## Slide 11: GRAPHICAL METHODS
The problems with this approach are (1) it is, to some extent, subjective; and (2) there is not a well-developed statistical theory for determining the small sample or asymptotic properties of the procedures.

## Slide 12: EMPIRICAL CDF
The sample cumulative distribution function (also called the empirical distribution function or empirical CDF) is a plot of the cumulative proportion of the data that lie below x, against x (- < x < ).

## Slide 13: EMPIRICAL CDF
The result is a step function, in this case a function having steps of height 1/n at each data point xi.
This is most easily done by use of the order statistics :

## Slide 14: EMPIRICAL CDF
Plot i/n versus x(i); then draw a horizontal line of height i/n from x(i) to x(i+1).
Alternatively, the ordinates can simply be connected to form a cumulative frequency polygon.
Both of these plots are nonparametric estimators of the population CDF, F(x) = P(X < x).

## Slide 15: PROBABILITY PLOTS
Different probability distributions lead to data that plot as different characteristic shapes in the CDF.These may or may not be easily recognizable or distinguishable in a plot of a given set of data. Probability plots have been developed as an alternative method of plotting data to overcome this problem.

## Slide 16: OTHER PLOTS
The idea (in a probability plot) is to transform the data and/or probability scales so that the plot on the transformed scale is linear (within chance fluctuations).
Equivalently, we plot sample fractiles against the fractiles of a specified distribution. As a result, the plots are sometimes referred to as “P-P Plots.”

## Slide 17: PROBABILITY PLOTS
Probability plotting papers have been developed for a number of distributions, including the normal and most of the important distributions used in reliability applications: exponential, lognormal, Weibull, gamma, and extreme value.
Many statistical computer packages (e.g., Minitab, SPSS, STAT, etc.) include some or all of these plotting options as well.

## Slide 18: PROBABILITY PLOTS
In interpreting the plots, we look for linearity as indicative of an adequate fit.
In addition, the plots may give an indication of potential outliers in the data, particularly if the overall pattern appears to be linear, but there appear to be a few points that lie outside this pattern.

## Slide 19: PROBABILITY PLOTS
Other anomalies that may be suggestive of specific model violations can also be found in the plots. For example, plots for which segmented lines (i.e., linear segments with different slopes) appear to fit the data suggest that a mixture model, which may result, for example, when multiple failure modes are present, may be appropriate.

## Slide 20: PROBABILITY PLOTS
Graphical analysis involves a good deal of judgment, especially in cases such as these. In the process, one often plots data on the various plotting papers available and then applies rough guidelines in an attempt to select one or more reasonable candidate models for the failure distribution.

## Slide 21: PROBABILITY PLOTS
The theory of probability plots involves the relationship between the x(i) and the corresponding fractiles of the selected distribution.
The plots are constructed by plotting the sample CDF corresponding to a given distribution against the x(i) after suitable transformation of one or both variables.

## Slide 22: PROBABILITY PLOTS
TWO ISSUES:
(i) Basis of the plot [Transformation needed]
(ii) Plotting the data: This depends on the type of data -- complete, censored, grouped
We look at the case of complete data.

## Slide 23: EXPONENTIAL DISTRIBUTION
p = F(x) = 1 - e-x
The p-fractile xp: xp = -1log[1/(1 - p)]
As a result, log[1/(1 - p)] plotted against xp will result in a linear relationship with intercept 0 and slope -1 = .
A probability plot is a plot of the transformed sample CDF versus x.

## Slide 24: WEIBULL DISTRIBUTION
The analysis similar to that for the exponential distribution and results in
log[log(1/(1-p))] = log(xp) - log()
Thus a plot of log[log(1/(1-p))] versus log(xp) is linear with slope .
In plotting, we use p = i/(n+1)

## Slide 25: HAZARD PLOT
The hazard (or failure rate ) function h(x) gives the instantaneous failure rate associated with a given distribution function. The cumulative hazard function H(x) is the integral of h(x), which yields H(x) = -log(1 - F(x)). Hazard plots are plots of the sample (or empirical) hazard function or cumulative hazard function.

## Slide 26: HAZARD PLOT
Hazard plots for complete data are constructed as follows:
(1) Form the order statistics.
(2) Calculate the hazard,
hi = 100/(n - i - 1), i = 1, ..., n.
(3) Calculate the
cumulative hazard

## Slide 27: HAZARD PLOT
(4) Plot x(i) versus Hi (or Hi versus x(i)) on either ordinary graph paper or cumulative hazard paper. Alternatively, the sample hazard function itself may be plotted by plotting hi versus x(i) on ordinary graph paper.

## Slide 28: GRAPHICAL ESTIMATION OF PARAMETERS
There are a number of approaches to obtaining parameter estimates based on the empirical CDF or the empirical cumulative hazard function.
They depend on the relationship between the fractiles of the distribution and its parameters, with the fractiles being estimated from the probability or hazard plots.

## Slide 29: GRAPHICAL ESTIMATION OF PARAMETERS
Note again that it is suggested that estimates of this type be used either as rough initial estimates or as starting points in numerical solutions of maximum likelihood equations (or both).
Fractiles may be read from graphs with free-hand lines or curves drawn or may be calculated from least squares fits to the plotted data.

## Slide 30: WEIBULL DISTRIBUTION
Parameters may be estimated using either cumulative hazard paper or a probability plot. In the former case, plot the data as usual and sketch a line through the data. Locate the dot in the upper left quadrant of the paper and draw a line through this point parallel to the sketched hazard line.

## Slide 31: WEIBULL DISTRIBUTION
The point at which this intersects the “shape parameter” scale at the top of the page is the estimate of . The estimate of the scale parameter  is the x-value corresponding to a cumulative hazard of H = 100.

## Slide 32: WEIBULL DISTRIBUTION
To use a probability plot for estimation of  and , the linearizing transformation on which the plot is based may be used. This is given by
The slope of the line on the cumulative hazard plot estimates , while the intercept estimates log(1/).

## Slide 33: WEIBULL DISTRIBUTION
Case 2.21:
We use the regression approach, with plotting positions of (i - 0.5)/n. Thus we regress yi = log[-log(1 - )] against log(xi). The results of the regression analysis (from Minitab) are as shown on the next page

## Slide 34: WEIBULL DISTRIBUTION
Regression Analysis
The regression equation is
y = - 21.0 + 16.1 log(x)
Predictor Coef Stdev t-ratio p
Constant -20.9955 0.2769 -75.82 0.000
log(x) 16.1140 0.2180 73.90 0.000
s = 0.08442 R-sq = 99.6% R-sq(adj) = 99.5%

## Slide 35: WEIBULL DISTRIBUTION
Analysis of Variance
SOURCE DF SS MS F p
Regression 1 38.925 38.925 5461.85 0.000
Error 24 0.171 0.007
Total 25 39.096

## Slide 36: WEIBULL DISTRIBUTION
The estimate of  is the slope of the line, i.e., 16.11.  is estimated as e21.00/16.11 = 3.68. Note that these are in very close agreement with the MLE’s, given in the annotation of Figure 11.4(b) of the text as * = 16.58 and * = 3.68.

## Slide 37: GOODNESS-OF-FIT
The classical test of this type is a Chi-Square test, which is appropriate for discrete data or grouped continuous data. In the continuous case, much more powerful tests are available for a few specific problems. Included are procedures that test specifically for the normal, exponential, Weibull and a few other distributions; and nonparametric tests that are used to test for any completely specified continuous distribution.

## Slide 38: GOODNESS-OF-FIT
Actual selection of a distribution based on a sample of data is often a mixture of art and science. Some of the suggested approaches are more powerful against specific alternatives and some are more powerful against others. If any of the tests rejects a particular distribution, particularly at  = .01 or less, that distribution should be rejected as a candidate life distribution.

## Slide 39: GOODNESS-OF-FIT
The only exception might be if it appears to provide a good fit in a graphical analysis, but there is evidence of possible outliers. In that case, a distribution should not be rejected if a good fit is obtained after removal of the outliers.
A good rule of thumb is that results should be used cautiously unless a good fit is found, and perhaps even then unless it is validated.

## Slide 40: DISCRETE DISTRIBUTIONS - THE CHI-SQUARE TEST
The classic Chi-Square test, due to Karl Pearson, may be applied to test the fit of discrete data to any specified distribution. The test statistic is

## Slide 41: DISCRETE DISTRIBUTIONS - THE CHI-SQUARE TEST
In the goodness-of-fit application of this test, we assume a sample of size n, with each observation falling into one of k possible classes. Oi is the observed frequency in class i; Ei is the frequency that would be expected if the specified distribution were the correct one.

## Slide 42: DISCRETE DISTRIBUTIONS - THE CHI-SQUARE TEST
In calculating , it is necessary to assure that expected frequencies are not too small; if they are, this may greatly distort the result. A rule of thumb is that if Ei < 1 for some i, combine that class with either the previous or the succeeding class, repeating the process until Ei  1 for all i. A conservative rule is to combine classes if Ei < 5.

## Slide 43: DISCRETE DISTRIBUTIONS - THE CHI-SQUARE TEST
Under the null hypothesis of a completely specified distribution (including parameter values), the test statistic has approximately a Chi-Square distribution with (k - 1) df. If r parameters are estimated from the data and the expected frequencies are calculated on this basis, the distribution of the test statistic is approximately a Chi-Square with (k - r - 1) df.

## Slide 44: DISCRETE DISTRIBUTIONS - THE CHI-SQUARE TEST
The test is an upper-tail test — large values of 2 result when observed and expected frequencies differ significantly, so these lead to rejection of the hypothesized distribution.

## Slide 45: CONTINUOUS DISTRIBUTIONS - THE CHI-SQUARE TEST
In applying the 2 analysis, the data are grouped into k intervals as in forming a frequency distribution and the expected frequencies are calculated as npi, where
where [Li-1,Li) is the ith interval, with L0 = - and Lk = .

## Slide 46: CONTINUOUS DISTRIBUTIONS - THE CHI-SQUARE TEST
As before, the intervals must be chosen so that Ei  1 (or 5), i = 1, …, k. If the distribution f(.) is completely specified, the resulting 2 has (k - 1) df.
As before, if r parameters are estimated from the data, df are k - r - 1.

## Slide 47: THE KOLMOGOROV-SMIRNOV (K-S) TEST.
The null hypothesis being tested is H0:F = F0. The test statistic Dn is simply the maximum distance between the hypothesised CDF and the empirical CDF. This is most easily calculated as Dn = max , where

## Slide 48: THE KOLMOGOROV-SMIRNOV (K-S) TEST.
The constants d are given in Table on the next slide for  = .15, .10, .05, and .01. The critical value of Dn is calculated as
Values of Dn in excess of the critical value lead to rejection of the hypothesised distribution.

## Slide 49: THE KOLMOGOROV-SMIRNOV (K-S) TEST.
Factors for Calculating Critical Values for the Kolmogorov-Smirov and Anderson-Darling Tests
   .15 .10 .05 .01
  d 1.138 1.224 1.358 1.628
  a 1.610 1.933 2.492 3.857

## Slide 50: THE ANDERSON-DARLING (A-D) TEST.
The Anderson-Darling test is also based on the difference between the hypothesised and empirical CDF’s. The test statistic is

## Slide 51: THE ANDERSON-DARLING (A-D) TEST.
Fractiles a of the distribution of are also given in the earlier Table. If the calculated value of exceeds a, the hypothesised distribution is rejected at level of significance . Note that the critical value a does not depend on n. Although this is an asymptotic result, it has been found to be a very good approximation in samples as small as n = 3.

## Slide 52: CONTINUOUS DISTRIBUTIONS [PARAMETERS UNKNOWN]
The goodness-of-fit problem is much more difficult when the parameters of the distribution are not specified in the null hypothesis.
A natural approach when H0 specifies only the form of the distribution is to use some method to estimate the parameters and then apply one of the above approaches.

## Slide 53: CONTINUOUS DISTRIBUTIONS [PARAMETERS UNKNOWN]
The problem is that the tests are no longer nonparametric in this case, and the distribution of the test statistic is very complicated, depending on the statistic, the estimation procedures used, the hypothesised distribution, and the true distribution.
Three basic approaches to the problem have been proposed. They are as follows:

## Slide 54: APPROACH 1
Embed the distribution in question in a larger family of distributions and test the null hypothesis that the parameter values are those that reduce the distribution to the one in question.

## Slide 55: APPROACH 1
For example, the Weibull distribution reduces to the exponential when the shape parameter  = 1, so a test for the exponential can be done by estimating the Weibull parameters and testing H0:  = 1.
A difficulty that has been encountered in using this approach is that the test may be powerful only against alternatives in the same family (e.g., other Weibull distributions).

## Slide 56: APPROACH 2
Determine the asymptotic distribution of the test statistic and use these results to obtain critical points. This has been accomplished for only a few distributions and has the added disadvantage that the results may not be appropriate for small samples.

## Slide 57: APPROACH 3
Use the tests discussed in the previous section, but use estimates of the unknown parameters and modify the critical values accordingly. This leads to some very difficult analytical problems, and the modified critical values are usually determined by means of simulation studies.

## Slide 58: MODEL SELECTION
The selection of a model in the context of reliability is the same as in any other application: it is a difficult problem and it involves art as well as science. If the modeler (analyst, engineer, manager, or other expert) truly understands the underlying structure, a model may be built on basic principles.

## Slide 59: MODEL SELECTION
More often than not, however, this is not the case, and the modelling process proceeds iteratively through many steps, a number of which involve data of many types. Each step in the process leads to an incremental improvement in the model and its relation to the real world.

## Slide 60: SELECTION OF A LIFE DISTRIBUTION
There is no definitive answer as to how a life distribution should be selected. A reasonable approach is the following:
  Perform goodness-of-fit tests to all feasible life distributions, estimating parameters from the data, testing for fit at the 1% level (or some alternative low level of significance). Any distribution rejected at this level should be considered an unacceptable model.

## Slide 61: SELECTION OF A LIFE DISTRIBUTION
  Any distribution not rejected should be considered to be a reasonable candidate model, and should be analysed further. If a physical model that accounts for the failure mechanism underlying a candidate distribution can be deduced and the parameters can be assigned a physical meaning, this model should be accepted.

## Slide 62: SELECTION OF A LIFE DISTRIBUTION
  Use Bayesian methods where appropriate to incorporate all relevant information into the decision process.
  If two or more candidate models fit the data and no other information is available, accept that all of these are possible models and check on the sensitivity of any estimators (e.g., of model parameters, reliability. etc.) to the distributions.

## Slide 63: SELECTION OF A LIFE DISTRIBUTION
  Calculate confidence limits for each parameter or other characteristic of interest under each distributional assumption.
  Compare the results and do a worst case analysis. This involves using the maximum upper confidence bound and minimum lower confidence bound for each parameter and considering these extremes as real possibilities. Make reliability decisions accordingly.

## Slide 64: SELECTION OF A LIFE DISTRIBUTION
  If these extremes are not acceptable, accept the fact that more data and/or other information will be required to arrive at a rational decision concerning the reliability of the item.
  Design and conduct an experiment that will provide the additional data needed, analyse the data, and continue the modelling process.