## Slide 1: RELIABILITY: CHAPTER 16
MAINTENANCE OF UNRELIABLE SYSTEMS

## Slide 2: SYSTEM DETERIORATION
All man-made systems are unreliable in the sense that their performance deteriorates with age and/or usage and they ultimately fail when they are unable to perform their required function under specified operating conditions.

## Slide 3: MAINTENANCE
Maintenance can be defined as actions to (i) control the deterioration process leading to failure of a system and (ii) restore the system to its operational state through corrective actions after a failure. The former is called “preventive” maintenance and the latter “corrective” maintenance.

## Slide 4: MAINTENANCE COST
Carrying out maintenance involves additional costs to the buyer and is worthwhile only if the benefits derived from such actions exceed the costs.
Maintenance is also of importance to manufacturers. “Maintainability” deals with maintenance issues during the design stage.

## Slide 5: APPROACHES TO MAINTENANCE
The approaches to maintaining unreliable systems have changed significantly since the beginning of this century.
Three different periods:
  - Pre 1940
  - 1940 - 1970
  - Post 1970

## Slide 6: PRE - 1940
Maintenance was viewed as an unavoidable cost and the only maintenance that was usually carried out was corrective maintenance.
Maintenance was neither incorporated into the design of the system, nor was the impact of maintenance on system and business performance duly recognised.

## Slide 7: 1940 - 1970
The evolution of Operations Research (OR) from its origin and applications during the Second World War to its subsequent use in industry led to the widespread use of preventive maintenance.
OR models for maintenance focus on the operational level by looking at costs and other performance metrics.

## Slide 8: POST 1970
A more integrated approach to maintenance evolved in both the government and private sectors.
A life cycle costing approach, with maintenance cost being a significant component, and the close linkage between reliability (R) and maintainability (M) was recognized.

## Slide 9: POST 1970 [Cont.]
This concept was also adopted by manufacturers and operators of civilian aircraft through the methodology of Reliability Centered Maintenance (RCM) in the USA.
Concurrently, the Japanese evolved a concept of Total Productive Maintenance (TPM) in the context of manufacturing.

## Slide 10: POST 1970 [Cont.]
Maintenance came to be viewed in the broader business context by taking into account the strong links between design, operation and maintenance.
Technical and commercial issues are integrated effectively and maintenance is viewed as being an important element of overall business performance.

## Slide 11: INFLUENCE DIAGRAM
Proposed by Vatn et al. (1996)
- Shows the effect of maintenance
- Views maintenance at different levels
- Shows the negative consequence of failures, and
- Final resulting consequences

## Slide 12
Component
quality
Maintenance
tasks
Logistics
(spare parts)
# of
failures
# on
demand
failures
Repair
time
Component
performance
#
Accidents
A
#
Accidents
B
Intermediate
system
performance
#
Downtime
hours
#
Shut-
Downs
#
Persons
injured
#
Persons
killed
Cubic m
pollution
Hours
Maint.
Ultimate
system
performance
Costs
Overall cost
=
Total Loss
Decision node
Performance node
Value node
2c.
3.
2b.
2a.
1.

## Slide 13: RCM [DEFINITION]
RCM is a discipline, method, logic or methodology used to identify preventive maintenance tasks to realise the inherent reliability of equipment at least expenditure of resources.
[Maintenance Steering Group]

## Slide 14: RCM METHODOLOGY
Involves consideration of the following:
1. system decomposition in terms of its components to the lowest part level,
2. identification of failure modes for each component,
3. determination of the importance of each component and of its failure, and
4. prioritizing preventive maintenance (PM) tasks that effectively reduce failure occurrence.

## Slide 15: RCM PROCESS
According to Moubray (1994), the RCM process involves asking the following seven questions (either for an existing operational system or a system yet to be built):
Q1: What are the functions and associated performance standards of the system in its present operating context?

## Slide 16: RCM PROCESS [Cont.]
Q2: In what way does it fail to fulfil its functions?
Q3: What causes each functional failure?
Q4: What happens when each failure occurs?
Q5: In what way does each failure matter?
Q6: What can be done to prevent each failure?

## Slide 17: RCM PROCESS [Cont.]
Q7: What should be done if a suitable preventive task cannot be found?
The RCM philosophy for PM is as follows:
“A preventive task is worth doing if it deals successfully with the consequences of failures which it is meant to prevent.”

## Slide 18: TPM
The Total Productive Maintenance (TPM) methodology evolved in Japan.
The need for avoiding equipment breakdowns during production was critical for the success of the JIT approach since breakdowns resulted in delays, and lowering of the yield and output quality, thus affecting customer satisfaction.

## Slide 19: TPM [Cont.]
These are assessed through the concept of Overall Equipment Effectiveness (OEE) and the costs resulting from six important losses.
OEE = Availability  Performance rate  Quality rate

## Slide 20: TPM [Cont.]
Low OEE is due to one or more of the following causes:
  availability being affected by (i) breakdowns and (ii) set-up and adjustments,
  performance rate being affected by (iii) idling and minor stoppages and (iv) reduced speeds, and
  quality being affected by (v) defects and rework and (vi) start-up losses.

## Slide 21: MAINTENANCE CONCEPT
This consists of statements and illustrations that define the theoretical means of maintaining equipment and relates tasks, tools, techniques and people in the maintenance process.
A proper understanding of the maintenance concept is essential for effective maintenance management.

## Slide 22: MAINTENANCE CONCEPT
Maintenance consists of the different functions (or activities) necessary to keep a system in, or restoring it to, an acceptable state (or operating condition).
Maintenance involves one or more of the following actions: Servicing, Testing/ Inspection, Removal/Replacement, Repair/Overhaul and Modification

## Slide 23: MAINTENANCE ACTIONS
Maintenance actions can be divided into the following two broad categories:
1. Corrective Maintenance (CM)
[Also called unscheduled maintenance]
2. Preventive Maintenance (PM)
[Also called scheduled maintenance]

## Slide 24: PREVENTIVE MAINTENANCE
Various Types:
Clock-based maintenance
Age-based maintenance
Usage-based maintenance
Condition-based maintenance
Opportunity-based maintenance
Design-out maintenance

## Slide 25: MAINTENANCE COSTS
Direct costs:
  cost of manpower
  cost of material and spares
  cost of tools and equipment needed for carrying out maintenance actions
  overhead cost
Various indirect costs

## Slide 26: OPTIMAL MAINTENANCE
With a low level of preventive maintenance effort, the PM cost is low but the expected corrective maintenance cost is high. As the PM effort is increased, the CM cost decreases and the PM cost increases.
Need for optimal trade-off.

## Slide 27
LOW
HIGH
P.M. EFFORT
COST
TOTAL COST
P.M. COST
C.M. COST
OPTIMUM P.M.EFFORT

## Slide 28: MAINTENANCE MODELS
Part or System Level
Objective function for determining the optimal maintenance policy
Information available - parameters of model, state of component, nature of inspection
Other issues: spares, repair facility, etc.

## Slide 29: PART-LEVEL MAINTENANCE
Failure distribution given by a failure distribution function F(t)
Non-repairable  failed items replaced by new ones
Repairable  Type of repair?
Inspection of state: Continuous or discrete

## Slide 30: PART-LEVEL MAINTENANCE
Time to repair or replace: Small relative to MTBF  can be ignored
Time horizon: Infinite ( use asymptotic results) or finite
Objective function: Expected or asymptotic; cost per unit time or availability per unit
Mean time to failure  (for a new item)

## Slide 31: NO PREVENTIVE MAINTENANCE
Replacement only on failure  failures occur according to a renewal process
Cost of each replacement Cf
Continuous inspection  failure detected immediately
Expected cost Jc(L) for finite L and asymptotic cost per unit time Jc (infinite L)

## Slide 32: NO PREVENTIVE MAINTENANCE
Finite L:
where M(t) is the renewal function given by

## Slide 33: NO PREVENTIVE MAINTENANCE
Infinite L:
This yields, with Jc = Cf/,

## Slide 34: RENEWAL REWARD THEOREM
Every failure is a renewal point and the interval between two successive renewal points defines a cycle.
where ECC is the expected cycle cost and ECL is the expected cycle length.

## Slide 35: AGE POLICY
The Age Policy is defined as follows:
Replace a component (under preventive maintenance) when it reaches age T (after being put into use) or on failure under corrective maintenance, if the item fails earlier.
Cf [Cp]: Cost of each failure [preventive] replacement

## Slide 36: AGE POLICY [Cont.]
Let Jc(L;T) denote the expected cost of maintaining a component over [0, L) starting with a new item at t = 0.
Conditional on the failure time of the first item X1 = x, we have

## Slide 37: AGE POLICY [Cont.]
On removing the conditioning
In the asymptotic case, we can use the Renewal reward Theorem to obtain an expression for Jc(T).
The results are as follows:

## Slide 38: AGE POLICY [Cont.]

## Slide 39: BLOCK POLICY
The Block replacement policy is defined as follows:
Replace the component at set times t = kT, k =1, 2, …, under preventive maintenance. Any failures in between these times are rectified through corrective maintenance, which involves replacing failed items by new ones.

## Slide 40: BLOCK POLICY [Cont.]
Asymptotic Cost per Unit Time Jc(T):
In this case the cycle length is deterministic and given by ECL = T and
ECC = Cp + Cf M(T)
This yields

## Slide 41: PERIODIC POLICY
This is applicable for repairable items and is defined as follows:
Replace items (under preventive maintenance) at times t = kT, k = 1, 2, .... Any failure between replacement times is repaired minimally.

## Slide 42: PERIODIC POLICY [Cont.]
The expected cycle length is ECL = T.
The expected cycle cost ECC is given by
As a result,

## Slide 43: SYSTEM-LEVEL MAINTENANCE
Many different model formulations
Preventive Maintenance: Discrete or continuous
Overhaul and Replacement options
Different objective functions
[See Blischke and Murthy (2000) for many review papers]

## Slide 44
AVAILABILITY
RELIABILITY
ENGINEERING
MAINTAINABILITY
ENGINEERING
LOGISTICS
OPERATIONS REQUIREMENT

## Slide 45: MAINTAINABILITY
A characteristic of design and installation which is expressed as the probability that the item will be retained in or restored to a specified condition within a given time period, when maintenance is performed in accordance with prescribed procedures and resources.
[MIL-STD-721]

## Slide 46: MAINTAINABILITY
A system effectiveness concept that measures the ease and rapidity with which a system or equipment is restored to its operational state after failing.
[Lalli and Packard (1997)]

## Slide 47: EFFECTIVE MAINTAINABILITY
The following questions are addressed:
  What parts have high failure rates?
  How can these failures be diagnosed easily?
  How quickly can the system be repaired?
  How much down-time is acceptable?
  What kind of preventive maintenance needs to be performed?

## Slide 48: LOGISTICS
Logistics can be defined as the art and science of management, engineering, and technical activities concerned with requirements, design, and planning and maintaining resources to support objectives, plans and operations.
A key issue in logistics is logistic support.

## Slide 49: LOGISTICS [KEY ELEMENTS]
Some of the key elements are:
Maintenance and support planning
Supply support (spare/repair parts and associated inventories)
Maintenance and support personnel
Training and training support
Test, measurement, handling, and support equipment
Maintenance facilities
Technical data, information systems and databases

## Slide 50: SPARES
Some of the issues are:
Quantities of spares needed over the life of the system
Optimal acquisition policies for spares
Location and delivery of spares when needed

## Slide 51: MMIS
Maintenance of a system is a complex process and effective maintenance requires proper coordination of many activities. A maintenance management information system (MMIS) is needed to carry out this coordination.
The MMIS must be capable of doing the following:

## Slide 52
  tracking components of the system being maintained,
  providing logistic support (e.g., spares inventory),
  storing maintenance history,
  alerting personnel with regard to predeter- mined maintenance activities at the correct time,
  performing an analysis of maintenance history,

## Slide 53
  determining optimal maintenance policies for items at different levels,
  combining maintenance activities into schedules,
  updating schedules as and when appropriate (e.g., on occurrence of an unexpected failure or event),
  planning resources, and
  measuring the effectiveness of maintenance activities.