## Slide 1: RELIABILITY: CHAPTERS 2 and 3
COLLECTION AND PRELIMINARY ANALYSIS OF FAILURE DATA

## Slide 2: DATA FOR RELIABILITY STUDIES
Historical Data
Vendor Data
Test Data
Handbook Data
Judgemental Data
Environmental Data
Field Data

## Slide 3: DATA FOR RELIABILITY STUDIES
Individual Item [system or component]
  Data on time to failure: Such data are variously called "failure data," "lifetime data”, "life data" or “complete data”
  Data relating to non-failures: Such data is called “service times”, "incomplete data” or “censored data”

## Slide 4: CENSORED DATA
TYPE I CENSORING: Censoring that occurs as a function of time is called Type I censoring. Put n items on test and stop the test at time .
Some fail and others are censored
Right or Left or Both Left and Right Censored Data
Singly or Multiply Censored Data

## Slide 5: CENSORED DATA
TYPE II CENSORING: Put n items on test and stop the test when a predetermined number r of failures have occurred (with r < n). This also results in incomplete data since the lifetimes of the remaining n - r items are not observed. This type of censoring is called Type II censoring.

## Slide 6: DATA FOR RELIABILITY STUDIES
Individual items
  Count data [failures over different time intervals]
Groups of items
  Pooled data
  Aggregate data

## Slide 7: RELIABILITY DATA [Case 2.1]

## Slide 8: RELIABILITY DATA [Case 2.1] [Cont.]

## Slide 9: RELIABILITY DATA
Case 2.2 Windshield Data
Comprised basically of several layers of material, including a very strong outer skin with a heated layer just beneath it, all laminated under high temperature and pressure.Failures of these items are not structural failures. Instead, they typically involve damage or delamination of the non-structural outer ply, or failure of the heating system. These failures do not result in damage to the aircraft, but do result in replacement of the windshield.

## Slide 11: RELIABILITY DATA
Case 2.3 Heart Pacemaker
Failure data for two manufacturers of heart pacemakers (Companies "A" and "B.") The data are on similar products for the two companies and were reported in January, 1996. During the period covered, Company A reported 272 faults and Company B, 255 faults.
No information regarding individual items, age at failure, items not failed etc.

## Slide 13: RELIABILITY DATA
Case 2.5: Industrial Products Sold in Batches
  Failure data is claims under warranty
  Items sold in batches
  Items returned for repair also as batches
  Various uncertainty: Age at failure, Number in use at any given time etc.

## Slide 15: RELIABILITY DATA
Case 2.7 Hydraulic System
The hydraulic components of large machines used in moving ore and rock (called load-haul-dump, or “LHD” machines) comprise a critical sub-system with regard to the reliability of this piece of equipment. Data were collected on time between consecutive failures (TBF) for such a system during the development phase, over a period of two years.

## Slide 17: RELIABILITY DATA
Case 2.8 Bus Motor Failures
Times to initial and subsequent failures of motors on buses in a large city fleet.
Failures considered are major breakdowns consisting of those which either caused the motor to be completely inoperative or to have insufficient power for operation of the bus. Minor failures were not included.

## Slide 19: RELIABILITY DATA
Case 2.14 Ball Bearing Data
The data is a set of measurements on fatigue failure of deep groove ball bearings. The data are taken from Lieblein and Zelen (1956), who provide a detailed analysis on just under 5,000 bearings tested by four companies over the period 1936 to 1951.

## Slide 21: RELIABILITY DATA
Case 2.18 Offshore Oil Exploration Equipment
The data are summary data only, giving number of units and number of failures observed in each category, with no indication of individual times to failure, number of failures per unit or other details

## Slide 23: RELIABILITY DATA
Case 2.22 Stress Fatigue Failures [Tungsten Alloy]
The data are experimental results on bend strength of a specimens of a brittle material, a tungsten carbide alloy containing 6% cobalt with ground surface finish.. Specimens were subjected to five different stress rates in a logarithmic progression from 0.1 to 1000 MN per square meter per second, with 12 specimens tested at each stress rate. The observed fracture stresses

## Slide 25: STATISTICAL INFERENCE
In data analysis, the most important objective is to be able to draw inferences from data in a meaningful way concerning population characteristics. Traditionally this is done through estimation of population parameters or other characteristics, and/or by testing hypotheses about parameter values.

## Slide 26: TYPES OF DATA
Scales of Measurement
Nominal Data
Ordinal Data
Interval Data
Ratio Data
The type of analysis to be used depends on the type of data.

## Slide 27: DESCRIPTIVE STATISTICS
In statistics, a parameter is defined to be a population characteristic, for example the mean time to failure (MTTF), . The corresponding quantity in a sample, e.g., the sample mean, is called a statistic.
More generally, a statistic is any quantity calculated from sample data.

## Slide 28: FREQUENCY DISTRIBUTIONS
A frequency distribution is a graphical or numerical description of an entire set of data. The objective is to present the data information in a concise form and in such a way that, if possible, the general shape of the distribution is displayed.
This not only makes the data more comprehensible, it can sometimes give some insights into structural issues.

## Slide 29: NUMERICAL FREQUENCY DISTRIBUTIONS
A numerical frequency distribution is a grouping of data into distinct categories or classes.
This is done by determining an appropriate number k of classes, determining appropriate class boundaries and simply counting to determine the frequency in each class.
Usually k is chosen to be between 5 and 20.

## Slide 30: CUMULATIVE FREQUENCY DISTRIBUTIONS
Cumulative frequency distributions are obtained by forming partial sums, that is, by summing frequencies over all classes up to and including a given class. Thus cumulative distributions give the number of values in the data set that are at or below a given value.

## Slide 31: RELATIVE FREQUENCY DISTRIBUTIONS
Relative Frequency Distributions. Division of the previous counts by the sample size n produces relative frequency and cumulative relative frequency distributions. These give, respectively, the proportion of values in a given class and the proportion in that class or below. Relative frequencies are often expressed in percents.

## Slide 32: DATA ORDERING
The set contains n data points (eg., failure times of n items)
The data are first ordered from smallest to largest (with ties, if any, included as repetitions), resulting in the set x(1), x(2), ..., x(n), forms the ordered data

## Slide 33: BOXPLOTS
A boxplot summarizes a set of data graphically on the basis of the Min, the three quartiles, so called because they divide the data into quarters, and the Max. The quartiles, Q1, Q2, and Q3, are determined as follows:

## Slide 34: QUARTILES
Q2, also called the median, is taken to be x((n+1)/2) if n is odd, and is calculated as [x(n/2) + x(n/2)+1]/2 if n is even. Q1 and Q3 are calculated as the medians of all points lying below and above the median, respectively.

## Slide 35: Data Set for Case (2.1) FREQUENCY DISTRIBUTIONS

## Slide 36: PARETO CHARTS
The Pareto chart is useful for displaying count data as proportions.
The importance of Pareto charts in the reliability context is in identifying the most frequently occurring, and hence usually most important, failure modes, separating out the "vital few from the trivial many" (the so called Pareto Principle).

## Slide 37: OTHER CHARTS
Pie Charts
Time Series Charts
  This is useful for studying variations occurring over time.
Higher Dimensional Plots

## Slide 38: MEASURES OF CENTRE
For many purposes (including statistical comparisons), summary statistics which convey essential characteristics of the data are required. The most common of such statistics, called variously measures of centre, measures of central tendency, measures of location, or simply means.

## Slide 39: MEASURES OF CENTRE
The most commonly used measure of centre is the sample mean, ,given by
Another common measure is the sample median, Q2

## Slide 40: MEASURES OF CENTRE
Although the mean and median are both measures of centre, a comparison of the two can give some information on another feature of the distribution, namely skewness. If > Q2, the distribution is skewed right; if < Q2, the distribution is skewed left. For symmetric distributions, the two measures are equal.

## Slide 41: MEASURES OF VARIABILITY
The second commonly used characteristic of a set of data is a measure of variability, spread, or dispersion. Measures of this type provide additional information concerning the distribution and further facilitate comparisons of different data sets.

## Slide 42: MEASURES OF VARIABILITY
The most common measures of dispersion are the variance and standard deviation. The sample variance, s2, is given by
The square root of this quantity is s, the sample standard deviation.

## Slide 43: MEASURES OF VARIABILITY
Another common measure of spread, used especially in quality control applications, is the sample range, calculated as Max - Min. The range, s2 and s are sensitive to outliers. A measure that is not is the inter-quartile range (IQR), defined previously as IQR = Q3 - Q1. The IQR is a measure of the spread of the middle 50% of the data.

## Slide 44: MEASURES OF VARIABILITY
The coefficient of variation (CV), calculated as s/ (often expressed as a per cent), is a unit-free measure of spread that is useful in comparing variables that differ in order of magnitude.
The Chebyshev Inequality is applicable to any distribution having finite variance. It states that at least a percent 100(1 - 1/k) of the distribution lies within k standard deviations of the mean, regardless of the shape of the distribution.

## Slide 45: FRACTILES
Fractiles (percentiles). The p-fractile of a distribution is a value xp having the property that at least a proportion p of the data lies at or below xp. xp is also called a percentile of the distribution. Examples are the three quartiles, Q1 , Q2, and Q3, which are, respectively, the .25, .50-, and .75-fractiles of the distribution. Other fractiles are calculated in a similar manner to that of the quartiles.