## Slide 1: RELIABILITY: CHAPTER 7
MODELING SYSTEM FAILURES

## Slide 2: PRODUCTS AND SYSTEMS
Most products and systems are composed of several components or parts.
Very simple products can be decomposed into several parts.
Several examples are discussed in Module 1.

## Slide 3: STEREO SYSTEM
SUB-SYSTEM 1
SUB-SYSTEM 2
SUB-SYSTEM 3
1
2
3
4
5
6
SPEAKERS
AMPLIFIER
TUNER / CD PLAYER / CASESSTE PLAYER

## Slide 4: PRODUCTS AND SYSTEMS
For complex systems, the number of parts may be very much larger. A multi-level approach to decomposition of such systems is required.
The number of levels that is appropriate depends on the system (or product) under consideration.

## Slide 5: MULTI-LEVEL DECOMPOSITION

## Slide 6: SYSTEM PERFORMANCE
The performance of the system depends on the state of the system (working, failed or in one of several partially failed states) and this in turn depends on the state (working/failed) of the various components.
By component we mean a unit at one of the lower levels -- part or an assembly.

## Slide 7: MODELING SYSTEM FAILURES
In the “black-box” approach, the state of the system is described either in terms of two states (working/failed) or more than two states (allowing for one or more partially failed states) without explicitly linking them to the components of the system.

## Slide 8: MODELING SYSTEM FAILURES
In the “white-box” approach, we model the state of the system specifically in terms of the states of the various components of the system.
We confine our attention to the case where each component is characterized by two states (working/failed).

## Slide 9: SYSTEM REPRESENTATION - I
A system can be represented schematically using special symbols or icons to represent the different components and connecting arcs which show the linkages between the components.
Example: Pneumatic pump

## Slide 10: SYSTEM REPRESENTATION - II
In the “block diagram” representation, each component is represented by a block with two end points.
When the component is in its working state, there is a connection between the two end points and this connection is broken when the component is in a failed state.

## Slide 11
b
(a)
k
1
2
n
a
a
b
(b)
1
2
n
a
b
(c)

## Slide 12: SYSTEM REPRESENTATION - II
A multi-component system can be represented as a network of such blocks with two end points.
The system is in working state is there is a connected path between the two end points. If no such path exists, then the system is in a failed state.

## Slide 13: SYSTEM REPRESENTATION - II
Block diagram representations are also called network representations.
It is worth noting that a block diagram representation is not a physical layout -- rather, it is a logical relationship between components which indicates the link between system performance and component performance.

## Slide 14: SYSTEM FAILURES
A system failure (either complete or partial) is due to the failure of one or more of its components.
Three types of failures:
(i) Primary failure
(ii) Secondary failure
(iii) Command fault

## Slide 15: SYSTEM FAILURES
Primary Failures:
A primary failure of a component occurs when the component fails due to natural causes (e.g., failing due to natural aging). An action (e.g., repair or replacement by a working unit) is needed to make the component operational.

## Slide 16: SYSTEM FAILURES
Secondary Failures:
A secondary failure is the failure of a component due to excessive stresses resulting from one or more of the following causes: (i) the (primary) failure of some other component(s) in the system, (ii) environmental factors, and/or (iii) actions of the user.

## Slide 17: SYSTEM FAILURES
Command Faults:
A command fault occurs when a component is in non-working (rather than a failed) state because of improper control signals or noise.
Often, no corrective action is needed to restore the component to its working state in this case.

## Slide 18: SYSTEM FAILURES
Independent vs Dependent Failures:
Since the different components of a system operate in the same environment, the failure times of the components are, in general, statistically dependent.
If the dependence is weak, they can be treated as being statistically independent.

## Slide 19: BLACK-BOX MODELING
Assumptions:
- Failures are independent
- Time to repair is negligible
- Failure of system is due to failure of a few components
- Repair (or replacement) of failed components has very little effect on the system condition (minimal repair).

## Slide 20: MODEL - I
The system failures are modeled by a point process with an intensity function (t;), with t representing the age of the system. (t;) is an increasing function of t, reflecting the effect of age. For example

## Slide 21: MODEL - II
Here we have major overhauls and minimal repair between overhauls. The failure rate after kth overhaul is given by k(t;), k = 0, 1, 2 , ....
k = 0 corresponds to a new system
For a fixed k, k(t;) is increasing in t
For a fixed t, k(t;) is increasing in k

## Slide 22: FAILURE RATE [With Overhauls]
k = 1
k = 2
k = 3
TIME
FAILURE RATE
OVERHAULS

## Slide 23: WHITE-BOX MODELING
Here the system failure is modeled in terms of the failure of the different components of the system. The linking of component failures to system failures can be done using two different approaches:
- Forward (Bottom-up) approach
- Backward (Top-down) approach

## Slide 24: WHITE-BOX MODELING
In the forward approach, one starts with failure events at the part level and then proceeds forward to the system level to evaluate the consequences of such failures on system performance. Failure mode and effects analysis (FMEA) uses this approach.

## Slide 25: WHITE-BOX MODELING
In the backward approach, one starts at the system level and then proceeds downwards to the part level to link system performance to failures at the part level. Fault tree analysis (FTA) uses this approach.

## Slide 26: FAILURE MODE AND EFFECTS ANALYSIS (FMEA)
1. Assist in selecting design alternatives with high reliability and high safety potential during the early design phase.
2. Ensure that all conceivable failure modes and their effects on operational success of the system have been considered.

## Slide 27: FAILURE MODE AND EFFECTS ANALYSIS (FMEA)
3. List potential failures and identify the magnitude of their effects.
4. Develop early criteria for test planning and the design of the test and checkout systems.
5. Provide a basis for quantitative reliability and availability analysis.

## Slide 28: FAILURE MODE AND EFFECTS ANALYSIS (FMEA)
6. Provide historical documentation for future reference to aid in the analysis of field failures and consideration of design changes.
7. Provide input data for trade-off studies.
8. Provide a basis for establishing corrective action priorities.

## Slide 29: FAILURE MODE AND EFFECTS ANALYSIS (FMEA)
9. Assist in the objective evaluation of design requirements related to redundancy, failure detection systems, fail-safe characteristics, and automatic and manual override.

## Slide 30: FMEA ANALYSIS
The basic questions to be answered by FMEA are the following:
[IEEE Standard 352]
1. How can each part conceivably fail?
2. What mechanisms might produce these modes of failure?

## Slide 31: FMEA ANALYSIS [Cont.]
3. What could the effects be if the failures did occur?
4. How is the failure detected?
5. What inherent provisions are provided in the design to compensate for the failure?

## Slide 32: FMEA ANALYSIS [Cont.]
For each component at the part level, the failure modes and their effects are usually documented on work sheets. The documentation involves the following:
- Description of different parts
- Characterisation of failures
- Effect of failures on other parts and on system performance

## Slide 33: FMEA ANALYSIS [Cont.] [Example]
Component: Bearings
Failure Modes:
- Lubrication loss (occurrence 45%)
- Contamination (30%)
- Brinelling (5%)
- Corrosion (5%)
- Other modes (15%)

## Slide 34: FMEA ANALYSIS [Cont.] [Example]
Component: Connectors
Failure Modes:
- Shorts (30%)
- Solder joints (mechanical) (25%)
- Insulator resistance (20%)
- Contact resistance (10%)
- Miscellaneous mechanical (15%)

## Slide 35: FMEA ANALYSIS
FMEA is usually carried out during the design phase. The objective is to reveal weaknesses and potential failures. This enables the design engineer to make appropriate modifications that may reduce the likelihood of failures and/or the seriousness of their consequences.
Computer packages are available.

## Slide 36: FAULT TREE ANALYSIS
A fault tree is a logic diagram that displays the relationship between a potential event affecting system performance and the reasons or underlying causes for this event. The reason may be failures (primary or secondary) of one or more components of the system, environmental conditions, human errors and other factors.

## Slide 37: FAULT TREE ANALYSIS
According to Fussel (1976) the value of a fault tree are as follows:
1. Directing the analysis to ferret out failures.
2. Pointing out the aspects of the system important to the failure of interest.
3. Providing a graphical aid in giving visibility to those in systems management who are removed from design changes.

## Slide 38: FAULT TREE ANALYSIS [Cont.]
4. Providing options for qualitative and quantitative system reliability analysis.
5. Allowing the analyst to concentrate on one particular system failure at a time.
6. Providing an insight into system behaviour.

## Slide 39: FAULT TREE ANALYSIS
A fault tree analysis involves the following steps:
1. Definition of the TOP event
2. Construction of the fault tree
3. Qualitative (and quantitative) analysis of the fault tree

## Slide 40: TOP EVENT
The Top event should always give answer to the following questions:
What: Describes the critical event that is the focus of attention
Where: Describes where the critical event occurs
When: Describes when the critical event occurs

## Slide 41: FAULT TREE CONSTRUCTION
The fault tree analysis is carried out by diagrams involving these two types of building blocks:
- gate symbols
- event symbols
- logical linking of these symbols

## Slide 42: QUALITATIVE ANALYSIS
The occurrence of the TOP event (i.e., system failure) is often due to different combinations of basic events (e.g., failures at the part level). A fault tree provides useful information about these different combinations. In this context, the concept of a cut set is very useful.

## Slide 43: QUALITATIVE ANALYSIS
A “cut set” in a fault tree is a set of basic events whose (simultaneous) occurrence results in the occurrence of the TOP event. A cut set is said to be minimal if the set cannot be reduced without losing its status as a cut set.

## Slide 44: RELATIVE COMPARISON
A fault tree has the following features that a FMEA does not have.
- Handles multi-point failures (cut sets with more than one element)
- Allows integration of causes of system faults
- Handles common-cause failures more easily.

## Slide 45: FAULT TREE AND BLOCK DIAGRAMS
A fault tree representation of a system can be easily converted into a block diagram representation and vice versa.
The block diagram representation is better suited for certain types of analysis.
One aspect of this analysis involves the concept of “structure function.”

## Slide 46: STRUCTURE FUNCTION
Let xi denote the state of component i,
i = 1, 2, ..., n.
Let x = (x1, x2,.....,xn) denote the state of the n components. Note this is a vector which can take one of 2n values.

## Slide 47: STRUCTURE FUNCTION
The state of the system is characterised by a binary valued function (x) where
(x) is called the structure function.

## Slide 48: STRUCTURE FUNCTION [Examples]
(x) depends on the system structure:
- Series Structure
- Parallel Structure

## Slide 49: STRUCTURE FUNCTION [Examples]
k-out-of-n system: System is in working state if at least k components are in working state. (x) is given by

## Slide 50: STRUCTURE FUNCTION [Examples]
k-out-of-n system: n = 3 and k = 2
This is obtained by representing the system in terms of series and parallel structures

## Slide 51: SYSTEM RELIABILITY
The structure function allows one to compute system reliability in terms of the component reliabilities when the component failures are statistically independent.
It can be extended to dependent failures but the analysis is more involved.

## Slide 52: SYSTEM RELIABILITY
Consider the case where all the components are non-repairable.
All the components are working at t = 0.
They fail independently and lead to system failure.
Let Xi(t) denote the state of component i at time t

## Slide 53: SYSTEM RELIABILITY
Let X(t) (a vector of Xi(t)) denote the state of the system. The system is in working [failed] state if (X(t)) = 1 [0], where  is the system structure function.

## Slide 54: SYSTEM RELIABILITY
For a component:
-Let Fi(t) denote the failure distribution for component i.
- Let pi(t) = P{Xi(t) = 1} = 1 - Fi(t)
- pi(t) is the reliability of component i
- E[Xi(t)] = pi(t)

## Slide 55: SYSTEM RELIABILITY
For the system
ps(t) = P{(X(t)) = 1} = 1 - Fs(t)
This can also be written as
ps(t) = E[(X(t))]
Since component failures are independent, we have
E[(X(t))] = (E[X(t)])

## Slide 56: SYSTEM RELIABILITY
As a result, we have
ps(t) = (p(t))
where p(t) is the vector of pi(t), i = 1, 2, ... n.
This relates system reliability to component reliability.

## Slide 57: STRUCTURE FUNCTION [Examples]
Series Structure:

## Slide 58: STRUCTURE FUNCTION [Examples]
Parallel Structure:

## Slide 59: RELIABILITY IMPORTANCE OF COMPONENTS
Birnbaum’s measure of the reliability importance of component i at time t is given by
This can be viewed as a “sensitivity” measure of system reliability with respect to component reliability at time t.

## Slide 60: MULTI-STATE MARKOV MODELS
The system consists of n components with each being either in working or failed state.
At any given time, the system can be in one of 2n states.
The failure and repair times (for all components) are exponentially distributed.

## Slide 61: MULTI-STATE MARKOV MODELS
Special case: n = 2 (Components A & B)
Four states for the system:
State Characterisation
1 A and B working
2 A working and B failed
3 A failed and B working
4 A and B failed

## Slide 62: MULTI-STATE MARKOV MODELS
The system failures (and repairs) can be modeled by a continuous time “Markov chain” formulation with 2n states.
One can derive expressions for various performance measures, such as availability, etc.

## Slide 63: DEPENDENT FAILURES
Since the components of a system share the same environment and the environment has an impact on the failure of components, failure times of components are not statistically independent.

## Slide 64: DEPENDENT FAILURES
Non-independent failures of n components of a system may be modeled by a multi-variate distribution function, defined as
The analysis of such models is, in general, more difficult.

## Slide 65: FAILURE INTERACTIONS
Often in a multi-component system, the failure of a component affects one or more of the remaining components of the system. This type of interaction between components is termed “failure interaction”.

## Slide 66: TYPES OF FAILURE INTERACTIONS
Type I failure interaction: whenever a component fails, it can induce the failure of one or more of the remaining components of the system
Type II failure interaction: whenever a component fails, it acts as a shock to one or more of the remaining components and affects their failure rate