## Slide 1: RELIABILITY: CHAPTER 1
INTRODUCTION TO BASIC CONCEPTS

## Slide 2: FAILURE [Common Usage]
According to the Random House Dictionary, failure is defined as "falling short in something expected, attempted, or desired, or to be in some way deficient or lacking".

## Slide 3: FAILURE [Definition - 1]
- "Failure is the termination of the ability of an item to perform a required function." [IEC 50(191)]
- "Equipment fails, if it is no longer able to carry out its intended function under the specified operational conditions for which it was designed." [Nieuwhof (1984)]

## Slide 4: FAILURE [Definition - 2]
"Failure is an event when machinery/ equipment is not available to produce parts at specified conditions when scheduled or is not capable of producing parts or perform scheduled operations to specification. For every failure, an action is required." [Society of Automotive Engineers ]

## Slide 5: FAILURE [Definition - 3]
Failure can be any incident or condition that causes an industrial plant, manufactured product, process, material, or service to degrade or become unsuitable or unable to perform its intended function or purpose safely, reliably, and cost-effectively. [Witherell (1994)]

## Slide 6: FAILURE [Definition - 3 (Cont.)]
This implies that the definition of failure should include operations, behaviour, or product applications that lead to dissatisfaction, or undesirable, unexpected side effects.

## Slide 7: PRODUCT CATEGORIES
Products can be categorised into three groups
Consumer durables
Industrial and commercial products, and
Specialised defence-related products.

## Slide 8: IMPLICATIONS OF FAILURE
When a failure occurs, no matter how benign, one feels its impact.
When the failure is catastrophic (as for example, in the crash of an aircraft or the collapse of a bridge) the total economic damage and loss of life can be very dramatic, affecting society as a whole.

## Slide 9: FAILURE OCCURRENCE
Failures occur in an uncertain manner and are influenced by factors such as design, manufacture or construction, maintenance and operation.

## Slide 10: FAILURE ELIMINATION?
There is no way failures can be totally eliminated. Every engineered object is unreliable in the sense that it will fail sooner or later even with the best design, construction, maintenance and operation. What can be done is to reduce the chance of occurrence of failures within a limited time frame.

## Slide 11: FAILURE CONTROL
This requires effective integration of good engineering with good management so that the failures and their consequences are minimised and the object can fulfil its intended purpose.

## Slide 12: FAILURE CONTROL [Cont.]
A proper study requires that we begin with a good and clear conceptual understanding and have a framework which allows us to integrate the various issues in an effective manner.

## Slide 13: SYSTEMS APPROACH
The Systems Approach provides the framework needed. An important feature of this approach is the use of mathematical models to obtain solutions to a variety of problems of interest to manufacturers and user-owners.

## Slide 14: SYSTEM AND PRODUCT DECOMPOSITION
Both products and systems can be decomposed into a hierarchy of levels, with the product or system at the top level and parts at the lowest level.

## Slide 15: EIGHT LEVEL DECOMPOSITION
  Level Characterisation
  0 System
  1 Sub-System
  2 Major Assembly
  3 Assembly
  4 Sub-Assembly
  5 Component
  6 Part
  7 Material

## Slide 16: EXAMPLES [Products and Systems]
1 Incandescent Electric Bulb
2 Hydraulic Operated Fail-Safe Gate Valve
3 Pneumatic Pump
4 Power Saw
5 Hot-chamber Injection System
6 Computer Hard Disk Drive (HDD)
7 Brake Mechanism for Train Wagons

## Slide 17: EXAMPLES [SYSTEM COMPLEXITY]
Example 1
Number of components in a farm tractor vs year of manufacture
Year 1935 1960 1970 1980 1990
Components 1200 1250 2400 2600 2900
Example 2
Boeing 747 airplane has 4.5 million parts.

## Slide 18: DIFFERENT FUNCTIONS OF A SYSTEM
1) Protective function: Protect people and environment from damage and injury.
2) Information functions: These comprise condition monitoring, gauges, alarms, etc.
3) Interface functions: This deals with the interface between the item under consideration and other items.
4) Superfluous functions: These are superfluous to the system. They occur due to modifications to a system which make an item no longer necessary.

## Slide 19: FAULT [Definition]
A fault is the state of the system characterised by its inability to perform the required function. A fault is hence a state resulting from a failure.

## Slide 20: FAILURE MODE [Definition]
A failure mode is a description of a fault. It is sometimes referred to as fault mode (for example, IEC 50(191)). Failure modes are identified by studying the (performance) function.

## Slide 21: FAILURE MODE CLASSIFICATION
1) Intermittent failures: Failures which last only for a short time.
2) Extended failures: Failures which continue until some corrective action rectifies the failure. They can be divided into
  a) Complete Failures which results in total loss of function.
  b) Partial Failures which result in partial loss of function.

## Slide 22: FAILURE MODE CLASSIFICATION [Cont.]
Each of these can be further subdivided into the following two:
  a) Sudden failures: Failures that occur without any warning.
  b) Gradual failures: Failures that occur with signals to warn of the occurrence of a failure.
A complete and sudden failure is denoted as Catastrophic failure and a gradual and partial failure is denoted as Degraded failure.

## Slide 23: FAILURE CLASSIFICATION

## Slide 24: FAILURE CAUSES [Definition]
According to the International Electrotechnical Commission [IEC 50 (191)] failure cause is "the circumstances during design, manufacture or use which have led to a failure".
Failure cause is useful information in the prevention of failures or their recurrence.

## Slide 25: FAILURE CAUSES
1) Design Failure
2) Weakness failure
3) Manufacturing failure
4) Aging failure
5) Misuse failure
6) Mishandling failures

## Slide 26: FAILURE CAUSES

## Slide 27: FAILURE SEVERITY [MIL-STD Classification]
1) Catastrophic: Failures that result in death or total system loss
2) Critical: Failures that result in severe injury or major system damage
3) Marginal: Failures that result in minor injury or minor system damage
4) Negligible: Failures that result in less than minor injury or system damage

## Slide 28: FAILURE SEVERITY [RCM Classification]
1) Failures with safety consequences
2) Failures with environmental consequences
3) Failures with operational consequences
4) Failures with non-operational consequences

## Slide 29: DETERIORATION [Definition]
Failure is often due to the effect of deterioration. The deterioration process leading to a failure is a complicated process. It varies with the type of product and the material used.

## Slide 30: FAILURE MECHANISMS [Classification]
Failure mechanisms can be divided into two broad categories
(i) Overstress failures
(ii) Wear-out failures.

## Slide 31: OVERSTRESS FAILURES
Overstress failures are as a result of one or more of the following: brittle fracture, ductile fracture, yield, buckling, large elastic deformation and interfacial de-adhesion.

## Slide 32: WEAROUT FAILURES
Wear-out failures comprises of failures due to wear, corrosion, dendtritic growth, interdiffusion, fatigue crack propagation, diffusion, radiation, fatigue crack initiation and creep.

## Slide 33: DETERIORATION PROCESS
The rate at which the deterioration occurs is a function of time and/or usage intensity.
An example of the different deterioration processes that lead to failures and the time-scales and usage factors that affect the rate of deterioration is given on the next slide

## Slide 34: AIRCRAFT BODY [Deterioration Processes]
Time-scale or Deterioration
usage intensity
1 Time in air Wear
Accumulation of fatigue
2 Number of landings Accumulation of fatigue (take offs) or flights High amplitude loading
3 Calendar year Corrosion

## Slide 35: JET ENGINE [Deterioration Processes]
Time-scale or Deterioration
usage intensity
1 Calendar year Corrosion
2 Operation time Wear
Accumulation of fatigue
3 # of operation cycles Temperature cycling
4 Time in take-off regime High temperature

## Slide 36: RELIABILITY [Definition -1]
Reliability of a product (system) conveys the concept of dependability, successful operation or performance and the absence of failures. Unreliability (or lack of reliability) conveys the opposite.

## Slide 37: RELIABILITY [Definition -2]
The reliability of a product (system) is the probability that the product (system) will perform its intended function for a specified time period when operating under normal (or stated) environmental conditions.

## Slide 38: RELIABILITY THEORY
Deals with the interdisciplinary use of probability, statistics and stochastic modelling, combined with engineering insights into the design and the scientific understanding of the failure mechanisms, to study the various aspects of reliability.

## Slide 39: RELIABILITY THEORY [Cont.]
It encompasses issues such as
    reliability modelling,
    reliability analysis and optimisation
    reliability engineering,
    reliability science,
    reliability technology and
    reliability management.

## Slide 40: RELIABILITY MODELLING
Reliability modelling deals with model building to obtain solutions to problems in predicting, estimating and optimising the survival or performance of an unreliable system, the impact of the unreliability, and actions to mitigate this impact.

## Slide 41: RELIABILITY ANALYSIS
Reliability analysis can be divided into two broad categories: (i) Qualitative and (ii) Quantitative. The former is intended to verify the various failure modes and causes that contribute to the unreliability of a product or system. The latter uses real failure data in conjunction with suitable mathematical models to produce quantitative estimates of product or system reliability.

## Slide 42: RELIABILITY ENGINEERING
Reliability engineering deals with the design and construction of systems and products taking into account the unreliability of its parts and components. It also includes testing and programs to improve reliability. Good engineering results in a more reliable end product.

## Slide 43: RELIABILITY SCIENCE
Reliability science is concerned with the properties of materials and the causes for deterioration leading to part and component failures. It also deals with the effect of manufacturing processes (eg. casting, annealing) on the reliability of the part or component produced.

## Slide 44: RELIABILITY MANAGEMENT
Reliability management deals with the various management issues in the context of managing the design, manufacture and/or operation of reliable products and systems. Here the emphasis is on the business viewpoint, as unreliability has consequences in cost, time wasted, and in certain cases the welfare of an individual or even the security of a nation.

## Slide 45: BRIEF HISTORY OF RELIABILITY
Prior to World War II, the notion of reliability was largely intuitive, subjective and qualitative.
A more quantitative (or mathematical) and formal approach to reliability grew out of the demands of modern technology and particularly out of the experiences in the second world war with complex military systems

## Slide 46: PRODUCT LIFE-CYCLE AND RELIABILITY
A product life cycle (for a consumer durable or an industrial product), from the point of view of the manufacturer, is the time from initial concept of the product to withdrawal of the product from the marketplace. It involves several stages.

## Slide 48: RELIABILITY OVER LIFE-CYCLE OF PRODUCT
The reliability of the product over the product life cycle may vary considerably but they involve various issues.
Technical
Operational
Commercial
Management

## Slide 49: RELIABILITY LIFE CYCLE
FEASIBILITY
DESIGN
DEVELOPMENT
PRE-PRODUCTION
PRODUCTION
LIFE OF ITEM
REPLACE /
DISCARD
R
E
L
I
A
B
I
L
I
T
Y
DESIGN LIMIT
TARGET VALUE
GROWTH
DETERIORATION
COST OF MAINTENANCE
TIME

## Slide 50: TECHNICAL ISSUES
Understanding of deterioration and failure [Material Science]
Effect of design on product reliability [Reliability Engineering]
Effect of manufacturing on product reliability [Quality variations and control]
Testing to estimate part and component reliability [Design of Experiments]

## Slide 51: OPERATIONAL ISSUES
Operational strategies for unreliable systems [Operations Research]
Effective maintenance [Maintenance Management]

## Slide 52: COMMERCIAL ISSUES
Cost and pricing issues [Reliability Economics]
Marketing Implications [Warranties, Service Contracts]

## Slide 53: MANAGEMENT ISSUES
Administration of reliability programs [Engineering Management]
Deciding on reliability issues from business viewpoint [Business Management]
Risk to individuals and society due to product unreliability [Risk Theory]
Effective management of these risks from a business viewpoint [Risk Management]

## Slide 54: RELIABILITY RELATED PROBLEMS
TWO PERSPECTIVES
- Buyer (Individual, Business, Government)
- Manufacturer
Depends on the product
- Consumer durables
- Commercial & Industrial Products

## Slide 55: MANUFACTURER’S PERSPECTIVE
From a manufacturer's point of view, the reliability of a product is influenced by several technical factors — design, materials, manufacturing, distribution, and so forth. Product reliability, in turn, affects the commercial side of the business — sales, warranty costs, profits.

## Slide 56: PRODUCT RELIABILITY
MATERIAL
PRODUCT
RELIABILITY
MANUFACTURE
DESIGN
QUALITY
CONTROL
WARRANTY COST
PROFITS
SALES

## Slide 57: VARIOUS ASPECTS
TECHNOLOGY
(MATERIAL, MANUFACTURING)
RELIABILITY
STATISTICS/PROBABILITY
STOCHASTIC PROCESSES
BUYERS
ENGINEERING
MANAGEMENT
MANUFACTURERS
SCIENCE
COMMERCIAL (BUSINESS)

## Slide 58: MANUFACTURER’S PERSPECTIVE
Problem 1: How is the reliability of parts or components estimated based on different types of data (failure or non-failure of items under test) obtained from testing?

## Slide 59: MANUFACTURER’S PERSPECTIVE
Problem 2: What is the appropriate relationship between reliability at normal and accelerated testing conditions? How should results be adjusted so that correct inferences under normal conditions can be drawn based on the results of the accelerated tests?

## Slide 60: MANUFACTURER’S PERSPECTIVE
Problem 3: What is the expected cost of servicing warranty for different types of warranties as a function of the reliability of the product?
Problem 4: What are the optimal warranty terms and pricing strategy, given the reliability of the product?

## Slide 61: MANUFACTURER’S PERSPECTIVE
Problem 5: How is the optimal reliability determined, taking into account product development, if the marketing strategy requires offering some specific warranty terms (e.g., a longer warranty period)?

## Slide 62: MANUFACTURER’S PERSPECTIVE
Problem 6: What is the number of spares needed to service a specific warranty? How does this change with the warranty duration?
Problem 7: What is the impact of process variations on the reliability of the product? How can these be con-trolled?

## Slide 63: BUYER’S PERSPECTIVE
INDIVIUALS
Problem 1: Is the extended warranty worth the price?
Problem 2: If warranty options are offered, which extended warranty policy best suits his/her needs?

## Slide 64: BUYER’S PERSPECTIVE [Cont.]
BUSINESSES
Problem 1: What maintenance policies are feasible and which policy is optimal?
Problem 2: How many spares are needed for different parts over the life of an item and what is the optimal purchase strategies for these spares?

## Slide 65: BUYER’S PERSPECTIVE [Cont.]
Problem 3: Economic decisions must be based on Life Cycle Cost (LCC), which includes not only the acquisition cost, but also the cost of maintaining and operating the system over its life cycle. How does one determine the LCC for different options and system reliability requirements?

## Slide 66: BUYER’S PERSPECTIVE [Cont.]
Problem 4: How is the actual reliability of the system delivered evaluated and compared with the reliability stated in the contract? What type of testing should be used?
Problem 5: How to evaluate different service contracts and select the most economical alternative?